## Slide 2: Autodesk Inventor Tips and Tricks for New Users
Jill Conlin, PLTW Teacher
College Station High School
College Station, TX

## Slide 3: Contact Information
Email: jconlin@csisd.org
Website: jconlin.weebly.com

## Slide 4: Downloading T9 Files
Download the T9 assembly
  Mypltw.org
    IED Teacher file
      Course Recourses
        Automoblox T9 Files

## Slide 5: Tips for Using the Main Menu
Customizing Standard Ribbon
  Right Click
    Show Panels
      Select the panel to be added
Reverse Mouse Wheel Zoom Function
  Tools
    Applications option
      Display
        Zoom Behavior, Click Reverse Direction

## Slide 6: Tips for Working with Part Files
Change Part Orientation
  Rotate to the view you want as Front
    Right click on View Cube
      Set Current View As
        Front
Precision Zooming
  Hold F3 to zoom in and out very small amounts
Using Multiple Windows for One Part/ Assembly
  View
    New
      Tile Vertically

## Slide 7: Tips for Working with Assembly Files
Visibility Shortcut (in Assembly)
  In the tree, Right Click on the part
    Type “V”
Copying Parts with a Drag/ Drop Method
  Find part/ subassembly in the tree
    Hold Control key and drag out from the tree
Selection Priority Tool
  Shift, Right Click
    Part Priority
Remove Appearance Overrides
  In the tree, Right Click Default
    Remove Appearance Overrides

## Slide 8: Tips for Working with Drawing Files
View Creation, Activate First
  To create a drawing of a part when multiples are open, click on the part file tab
    Create Base View, now your part will automatically show in the View Creation
Control Key for Section View
  Click on Section View
    Pick the View
      Draw section line, Continue
        Hit Control key and now it will move out of alignment

## Slide 9: Creating a Custom Title Block
Open a new Drawing file (Standard.dwg).
Change the paper size by right clicking on Sheet 1 in the Browser, left clicking on Edit Sheet, selecting A under Size, and clicking OK.
Right click on the ANSI Large title block and delete.
Navigate to Title Blocks by clicking the + next to the Drawing Resources folder in the browser. Right click on Title Blocks and select Define New Title Block.

## Slide 10: Creating a Custom Title Block Cont.
Now use sketching tools (rectangle, line, etc.) to create outlines of how you want the title block sections to look
Use the text tool to place text in your title block.
  To create permanent text, left click to locate top left corner of the text. Type in the text desired. Highlight the text in order to change font size, bold, etc. Select OK.
  To create Prompted Entry text, left click to locate top left corner of the text. Under Type, select Prompted Entry. Replace the text that says Enter Prompt for Field with your prompt. Highlight your prompt to change font size, etc. Click OK when done
  To use field text (automatic info), left click to locate top left corner of the text. Under Type, select the property you want to use, and then click the Add Text Parameter button. Do not edit the text in the text box. Highlight text to change font, bold, etc. Click OK.

## Slide 11: Creating a Custom Title Block Cont.
To insert an image, make sure your image is a bitmap. From Insert panel select Insert Image (icon that looks like a mountain). Left click to locate image and bring up Open pop up. Make sure to uncheck Link in the open window, or you will have to include any images that you use in the Templates folder.
When done creating/editing your block, right click and Save Title Block.
In your browser double click on the block that you have created. This action will apply the block to your drawing. If prompted entry appears, hit Cancel.

## Slide 12: Creating a Custom Title Block Cont.
Save As and then choose Save Copy As Template. Save file in Inventor Templates folder OR have students save this template on their network drive space. This can now be opened and used as their template for any drawing file they create. If you wish to create a new tab in the New File box, create a new folder within the Templates folder. Save any items that you want to include in that folder.

## Slide 13: Recap & Questions?
Email: jconlin@csisd.org
Website: jconlin.weebly.com